## Slide 1
AudiaHybrid
Hybrid RF–Optical Assistive Listening & Real-Time Telemetry Platform
Phase 1: digital text link · Phase 2: voice
Cyril Raj · Reg. No. 2510040085 · Section 1
B.Tech ECE, Year 2 · KLH Aziznagar
Course 25SC2008E · Full Stack Web Development
Notes: Introduce the project and the plan: build and prove a digital text link first, then add voice on the same hybrid link.

## Slide 2
The problem: one link is never enough
Assistive listening devices usually rely on a single medium
AudiaHybrid · Cyril Raj · 2/10
Radio frequency (433 MHz)
Passes through walls (non-line-of-sight)
Longer range
Prone to interference and congestion
Signal leaks outside the room: weak privacy
Optical (LED light)
Immune to RF noise
Stays in the room: private
Needs line of sight
Ambient light can saturate the receiver
Our answer: send over both links at once. Phase 1 is a text link: you type a message on the dashboard, the ESP32 sends it as light and radio together, checks it with a CRC and reports which link delivered it. Voice follows once the text link works.
Notes: RF and optical have opposite strengths and weaknesses. Use both, and decide between them with live data.

## Slide 3
System architecture (Phase 1)
A message travels the hybrid link and the result comes back to the dashboard
AudiaHybrid · Cyril Raj · 3/10
Dashboard
Type a message to send
›
ESP32 sends
Adds CRC, drives LED and 433 MHz TX
›
Two links
White LED light + 433 MHz radio
›
ESP32 receives
Decodes both, checks CRC
›
Broker + backend
MQTT → SQLite → dashboard
Same board, both ends
One ESP32 transmits and receives in the demo
Built and tested in Wokwi first
Result path
Delivery result sent over MQTT
Backend stores it in SQLite
Dashboard shows badge, success rates, event log
Ready for voice
Phase 2 reuses the broker, backend and dashboard
Notes: One ESP32 sends and receives in the demo. The broker carries the results to the backend and the dashboard.

## Slide 4
Plan: text first, then voice
Two phases on the same hybrid link
AudiaHybrid · Cyril Raj · 4/10
Phase 1: digital text link (now)
Type a message on the dashboard
Sent as LED pulses and 433 MHz together
CRC check; reports which link delivered
No capacitors; parts already on the list
Phase 2: voice (next)
Mic → LM741 preamp → 300 Hz–3.4 kHz filter
LED driver and 433 MHz transmitter
Photodiode and RF receivers, LM386 to headphones
Needs capacitors and more tuning
Why it matters: a small copy of real hybrid links such as Li-Fi with Wi-Fi backup. Text captions also suit hearing-impaired users.
Notes: Why text first: simpler hardware, and the CRC gives measurable success rates per link. Voice reuses the software.

## Slide 5
Phase 1: how the text link works
ESP32 · LED · 433 MHz modules · CRC
AudiaHybrid · Cyril Raj · 5/10
Message flow
Type a message on the dashboard
ESP32 frames it and adds a CRC
LED pulses and 433 MHz are sent together
Both receivers decode the message
CRC check; delivering link is noted
Result goes MQTT → backend → dashboard
Pin | Role | Detail
GPIO25 | LED | White LED transmit
GPIO26 | RF TX | 433 MHz transmit
GPIO34 | Optical RX | Light receiver
GPIO35 | RF RX | 10k/10k divider
Wiring rules
Never exceed 3.3 V on an ESP32 pin
GPIO34/35 are ADC1: fine with Wi-Fi on
Notes: Walk through the six steps, then the four pins. The 10k/10k divider protects the ESP32 input.

## Slide 6
Phase 2: voice
Added after the text link works
AudiaHybrid · Cyril Raj · 9/10
Analog audio chain
Electret mic with LM741 preamp (≈20–40 dB)
Band limit 300 Hz – 3.4 kHz, tone control
LED driver and 433 MHz AM transmitter
BPW34 photodiode receiver with amplifier
RF receiver with envelope demodulator
LM386 amplifier to headphones
Carries over
MQTT, backend, dashboard
Failover rule between links
New in Phase 2
Capacitors and tuning
RF audio quality is the main risk
Notes: The voice phase is the original design from the reports. The main risk is that 433 MHz modules are made for digital data.

## Slide 7
Failover and live demo
Simulate in Wokwi first, then repeat on the real hardware
AudiaHybrid · Cyril Raj · 6/10
Failover rule
Cover the LED: the system switches to RF automatically
Uncover it: it returns to optical
Dashboard badge shows the active link
Audio is sent on both links at once: LED and 433 MHz RF
ESP32 checks both link levels every 500 ms
Analog switch routes the live link to the LM386 headphone amp
Demo script
Send HELLO
Speak into the mic: audio plays on optical
Cover the LED
Watch the badge flip to RF
Audio keeps playing, now over RF
Show success rates and event log
Simulation first
Wokwi proves ESP32 → MQTT → dashboard before wiring
Pots and a switch stand in for the links
Wokwi cannot run the analog circuits
Real audio runs only on hardware: mic → preamp → filter → LED + RF
Receivers → switch → LM386 → headphones
Notes: Demo order: send HELLO, cover the LED, show the badge flip to RF, then success rates and the event log.

## Slide 8
MQTT data contract
The agreement between firmware, backend and dashboard
AudiaHybrid · Cyril Raj · 7/10
Item | Value
Broker | broker.hivemq.com
ESP32 port | 1883 (TCP)
Browser port | 8884 (secure WebSocket)
Telemetry | audiahybrid/cyril-raj/telemetry
Status | …/status (retained, online/offline)
Rate | Every 500 ms
{
"optical": 2840,
"rf": 1920,
"opt_ok": true,
"rf_ok": true,
"preferred": "optical",
"active": "optical",
"rssi": -55
}
Last-will: the broker publishes “offline” if the ESP32 disappears. Text-link fields (message, CRC result, delivering link) will extend this packet.
Notes: If any one side changes a field name, the other two break, so the contract is written down and shared.

## Slide 9
Backend and web dashboard
Node.js · Express · Prisma · SQLite | React 18 · Vite · Tailwind
AudiaHybrid · Cyril Raj · 8/10
Backend
MQTT subscriber, stores at most 1 row/second
Socket.io and SSE push live data
REST: /api/hardware/readings, /history, /summary, /status, /health
Status service flags stale links
Dashboard (4 pages)
Dashboard: live panel, tiles, charts, event log
Telemetry: transport choice, backend health
Records: 1 h / 24 h / 7 d history, CSV export
About: signal chain, design vs prototype
Notes: The backend bridges MQTT to storage and live streams. The live hardware panel also talks to MQTT directly.

## Slide 10
Results, limits and future work
AudiaHybrid · Cyril Raj · 10/10
Verified
Firmware builds in both modes
Client builds, 24 tests pass
Live loop: ESP32 → HiveMQ → dashboard and database
Limitations
Public broker has no login
Simulation uses pots, not real signals
Physical text-link build is still in progress
RF modules suit digital data, not audio
Future work
Build and measure the text link
Voice over the same hybrid link
Authenticated, encrypted MQTT
PostgreSQL, login, deployment
Text first, voice next: one hybrid link, one decision rule, live visibility.
Notes: End on the honest picture: what is verified, what is limited, and what comes next.